## Slide 1: Codes

## Slide 2: Binary code for Decimal number
Binary code are appropriate for internal computation of a digital system
People prefer to deal with decimal number
External interface of a digital system accepts/process/displays decimal number directly
Binary code for decimal digit requires minimum four bits.
Different code can obtain by arranging four or more bit
Binary Code
Weighted Code
Non Weighted Code
each position of the number represents a specific weight
Binary Code, Octal Code, Decimal Code, Hexadecimal code,
Binary Coded Decimal (BCD) Code
each position within the binary number is not assigned a fixed value
Excess3 code, Gray code

## Slide 3
Notes: Any information, maybe a character, an image or audio, need to be converted to a sequence of zeros and ones in order to be stored in computers.

## Slide 6
Notes: https://www.youtube.com/watch?v=ZNFyOSHh8P0

## Slide 13
Table gives the four‐bit code for one decimal digit. A number with k decimal digits will require 4k bits in BCD.
Decimal 396 is represented in BCD with 12 bits as 0011 1001 0110, with each group of 4 bits representing one decimal digit.
A decimal number in BCD is the same as its equivalent binary number only when the number is between 0 and 9.
A BCD number greater than 10 looks different from its equivalent binary number, even though both contain 1’s and 0’s. Moreover, the binary combinations 1010 through 1111 are not used and have no meaning in BCD.

## Slide 17
It is important to realize that BCD numbers are decimal numbers and not binary numbers, although they use bits in their representation.
The only difference between a decimal number and BCD is that decimals are written with the symbols 0, 1, 2, c, 9 and BCD numbers use the binary code 0000, 0001, 0010, c, 1001.
The decimal value is exactly the same.
Decimal 10 is represented in BCD with eight bits as 0001 0000 and decimal 15 as 0001 0101.
The corresponding binary values are 1010 and 1111 and have only four bits.

## Slide 19
Set of n-bit string represent a number called code
A particular combination of n-bit value is codeword
BCD (Binary coded Decimal) is straight assignment of binary equivalent
BCD code ranges from 0-9
Excess-3 code is self complimentary code
Decimal Digit | BCD Code 8 4 2 1 | Excess-3 | 8 4 -2 -1 | 2 4 2 1

## Slide 20: BCD
BCD the binary number formed by four bit 0000-1001
Each digit represented by separate 4 bit
BCD, is process for converting decimal numbers into their binary equivalents
Advantage
Allows easy conversion between decimal and binary form.
Disadvantage
States between 1010 (decimal 10), and 1111 (decimal 15) are not used.
35710 = 0011 0101 0111 (BCD)
8510 = 1000 0101 (BCD)
57210 = 0101 0111 0010 (BCD)
857910 = 1000 0101 0111 1001 (BCD)
Decimal to BCD
BCD to Decimal
10012 = 1001BCD = 910
10001112 = 0100 0111BCD = 4710
10100111000.1012 = 0101 0011 0001.1010BCD = 538.62510

## Slide 25: XS-3 code
A non-weighted BCD code
A 4-bit code
A sequential code
Each binary codeword is corresponding to 8421 code + 0011.
Has 6 invalid states (0,1,2,13,14,15)

## Slide 27: Excess-3 Code
Made by adding 3 with the equivalent decimal of a binary number and again converting into binary

## Slide 28: XS-3 codes are self-complementing

## Slide 29: How to check whether weighted codes are self-complementing or not?
Add the weights of all 4 bits.
If sum = 9, only then it is self complementing

## Slide 39: Gray Code
A non-weighted code
A cyclic code
Not a BCD code
Not suitable for arithmetic operations

## Slide 41: How does Gray code reduce switching operations?

## Slide 46: Convert binary 0110 to Gray code.

## Slide 49: Convert Gray 0101 to binary code.

## Slide 52
Convert Binary code 100101 to Gray

## Slide 53
Feature of GRAY code is
a) All digits change between counts b) Two digits change between counts c) Only one digit changes between counts d) Alternate digit changes between counts
Quiz